## Slide 1: A Sequential Codelet Model for parallel program Execution
Jose Manuel Monsalve Diaz
Notes: A parallel machine model through hierarchical codelet definition

## Slide 2: This presentation
Motivation
  Brief History of Sequential Computing
  Sequential computing infrastructure
  Parallelism In current systems
  Problem statement and goals
Sequential computation. Lessons learned
Parallel Turing Machine definition
Sequential Codelet Model
  Single level SCM Abstract Machine
  Exploiting parallelism in the SCM Abstract Machine
  Hierarchical SCM Abstract Machine
Examples
  Dot Product
  1D Convolution

## Slide 3: MOTIVATION

## Slide 4: How did we get here?
1936
Turing Machine
1945
Von Neumann Architecture
1960
ISA (IBM 360)
1973
Writable Control Store
Software
Hardware
1979
1981
1985
Intel 8086
IBM PC
Intel 80386
1966
CDC6600
1969
Unix
1983
C++
1972
C
2004
Intel Tejas (Cancelled)
1991
MPI 1
1998
OpenMP 1.0
1995
POSIX Threads
1949
Short Code
1957
FORTRAN
Large distance between hardware and software abstractions
1986
AIX OS
Based on Hennessey and Patterson Turing Lecture:
A New Golden Age for Computer Architecture
Notes: Add AIX IBM Operating System
MULTICS Virtual Memory
Add at the bottom of this slide: Cite the H&P Turing award paper
Two dimensional timeline

## Slide 5: How did we get here?
1936
Turing Machine
1945
Von Neumann Architecture
1960
ISA (IBM 360)
Software
Hardware
All our General Purpose computation ecosystem is based off these three models which are purely sequential

## Slide 6: computer Systems Infrastructure
U S E R S / P R O G R A M M E R S
PROGRAMMING ENVIRONMENTS
EXECUTION ENVIRONMENTS
DYNAMIC LIBRARIES
LOADERS
RUNTIMES AND OS SCHEDULERS
H A R D W A R E
HIGH LEVEL PROGRAMMING LANGUAGES
(C, C++, FORTRAN, JAVA)
SOFTWARE PACKAGES, LIBRARIES, UTILITIES
COMPILERS
TOOLS & SDKs
RUNTIME SYSTEM
HARDWARE
HARDWARE PROGRAMMING API
Notes: There is a large discussion on how to fill in this gap

## Slide 7: Parallelism in current systems
Implemented Architecture
Turing Machine
Von Neuman Architecture
Software infrastructure
Processes and Threads
Parallel abstraction model
Runtime Systems
Parallel prog. models
ISA
Implicit Parallelism (ILP)
Pipelining
Superscalar
Out of Order Execution
Register Renaming
Explicit Parallelism (User defined)
Multiple Processes
  MPI
Multiple Threads
  OpenMP
  SYCL
Higher level programming abstractions
  Tensorflow

## Slide 8: Problem Statement
Based on the lessons learned from sequential computation, is it possible to define an implicitly parallel program execution model that extends through the whole computation system (not limited to a single core)?

## Slide 9: Goals
Define a program execution model, with its respective abstract machine which:
  Is easy to reason about for the programmer,
  Uses the memory and system hierarchy
  Allows parallelism
  Allows heterogeneity
  Enable us to use all the experience gather throughout the years in sequential computation
    Correctness
    Quantitative program execution analisys
    Other properties of sequential execution…

## Slide 10: SEQUENTIAL COMPUTATION Lessons learned

## Slide 11: 5 Stages Pipeline architecture
FETCH
DECODE
EXECUTE
MEMORY
WRITE BACK
Adder
Inst
Memory
Reg File
Sign Extend
Memory
ALU
Zero?
MUX
MUX
MUX
MUX
ADDRESS
IF/ID
EX/MEM
MEM/WB
ID/EX
Next PC
Next seq PC
Next seq PC

## Slide 12: 5 Stages Pipeline architecture
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem

## Slide 13: ALU Operations
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem
Supported operations are a tradeoff between:
Application
Chip Area
Feature size
Required on-chip memory
System cost
…

## Slide 14: ALU Operations
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem
ALU Operations execution time are not dependent on the memory access time.
Tcompute >> Tmemory

## Slide 15: 5 Stages Pipeline architecture
L0 Register File
Extending the EU
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem

## Slide 16: Hierarchical Turing Machine

## Slide 17: Hierarchical Turing Machine
 | Ω | ℌ | ℥ | Ω | ℥ | 
READING HEAD
State evaluation unit
Ω
℥
Ω
℥
State machine (codelets)
S1
S2
S3
S4
Level N Infinite tape memory
S3
Current state LN-1
Executing State
Level N-1 Infinite tape memory
LEVEL N
LEVEL N-1
READING HEAD
State evaluation unit
Ω
℥
Ω
℥
State machine (codelets)
K1
K2
K3
Level N-2 Infinite tape memory
LEVEL N-2
…
K1
Current state LN-2
…
Current state LN
Each level is a complete Turing machine, with an additional state evaluation unit and an infinite memory tape.
The state evaluation unit is a complete Turing machine, that uses the infinite memory tape of the level above as its memory storage.
A state is defined in terms of a Finite state machine that is evaluated in the state evaluation unit of the level below
Notes: Petri Net Thesis. Allows the system on multiple states
Although the definition of a state and its transition is sequential in the sense that it will transition to only one single state to follow. However, it allows parallel execution in the hardware implementation.

## Slide 18: Sequential Codelet Model

## Slide 19: Sequential Codelet Model
L1 Register File
L0 memory
L0
Arithmetic operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem
L0
L1

## Slide 20: Codelet Definition
A Codelet is an instruction that is well defined in terms of resources.
  Required memory
    Inputs, Outputs and Operation
  Computational complexity
    Bounded execution latency
A Codelet is executed when all the required resources are available:
  Data dependencies
  Structural dependencies
A Codelet is executed atomically
A Codelet is non-preemptive
A Codelet is defined in terms of other codelets or lower level hardware instructions

## Slide 21: Single Level SCM Abstract Machine

## Slide 22: Abstract machine Sequential (single core)
L1 Sequentia Codelet Abstract Machine
Reg File
EXECUTE
(Current Architectures)
SU
FETCH
DECODE
Write Back
Synchronize
Memory Interface
MEMORY

## Slide 23: Abstract machine Sequential (single core)
L1 Sequentia Codelet Abstract Machine
Reg File
EXECUTE
(Current Architectures)
SU
FETCH
DECODE
Write Back
Synchronize
Memory Interface
MEMORY

## Slide 24: Abstract machine Parallelism – II (Superscalar)
L1 Sequentia Codelet Abstract Machine
Current core Architecture
(EXECUTE)
Current core Architecture
(EXECUTE)
Reg File
EXECUTE
(Current Architectures)
SU
FETCH
DECODE
Write Back
Synchronize
Memory Interface
MEMORY

## Slide 25: Abstract machine Heterogenity
L1 Sequentia Codelet Abstract Machine
Current core Architecture
(EXECUTE)
Current core Architecture
(EXECUTE)
Reg File
EXECUTE
(Current Architectures)
SU
FETCH
DECODE
Write Back
Synchronize
Memory Interface
MEMORY
GPU-Like core
CPU-like core
CSA-Like core

## Slide 26: Abstract machine Parallelism – III (Out-of-order execution)
L1 Sequentia Codelet Abstract Machine
Current core Architecture
(EXECUTE)
Current core Architecture
(EXECUTE)
Reg File
EXECUTE
(Current Architectures)
SU
FETCH / DECODE
Reordering buffer
Write Back
Synchronize
Re-ordering
Memory Interface
MEMORY

## Slide 27: Abstract machine Parallelism – IV (Register renaming)
L1 Sequentia Codelet Abstract Machine
Current core Architecture
(EXECUTE)
Current core Architecture
(EXECUTE)
Reg File
EXECUTE
(Current Architectures)
SU
FETCH / DECODE
Renaming
Write Back
Synchronize
Renaming
Memory Interface
MEMORY

## Slide 28: Abstract machine Parallelism – V (SIMD)
L1 Sequentia Codelet Abstract Machine
Current core Architecture
(EXECUTE)
Current core Architecture
(EXECUTE)
Reg File
VECTOR EXECUTION
(Current Architectures)
SU
FETCH / DECODE
Renaming
Write Back
Synchronize
Renaming
Memory Interface
MEMORY

## Slide 29: Abstract machine A parallel program
LD
LD
It can be expressed sequentially as an ISA:
LD R1 ADDR1
LD R2 ADDR2
OP1 R3 R1 R2
OP2 R3 R4
OP2 R3 R5
OP3 R3 R6
OP3 R3 R7
OP1
OP2
OP2
OP3
OP3

## Slide 30: Hierarchical SCM Abstract Machine

## Slide 31: Deepening the hierarchy Can we go an extra level?
MEMORY

## Slide 32: Deepening the hierarchy Can we go an extra level?
Current core Architecture
(EXECUTE)
Current core Architecture
(EXECUTE)
Reg File
EXECUTE
(L1 CSM)
SU
FETCH / DECODE
Renaming
Write Back
Synchronize
Renaming
Memory Interface
MEMORY
MEMORY
L1 Sequentia Codelet Abstract Machine

## Slide 33: Hierarchical SCM Abstract Machine
A program is defined hierarchically, mapping to each level of the SCM Abstract Machine
Each level behaves as an ISA that maps to execution units in the level below.
Memory operations LD/ST are issued to the level above, guaranteeing low latency
Memory allocation at a certain level is done through register allocation
L2 Register File
L1 memory
L1
Higher level operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem
L1 Register File
L0 memory
L0
Arithmetic operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem
To higher level mem
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
Inst Mem
L0
To higher levels
L1
L2

## Slide 34: Codelet Definition Revisited
A Codelet is an instruction that is well defined in terms of resources.
A Codelet is executed when all the required resources are available:
A Codelet is executed atomically
A Codelet is non-preemptive
A Codelet is defined in terms of other codelets or lower level hardware instructions
A Codelet is mapped to a level of the hierarchy defined by the Sequential Codelet Model

## Slide 35: Examples

## Slide 36: A Dot Product Example

## Slide 37: Dot Product
.
=
A
B

## Slide 38: Dot Product
.
=
A
B

## Slide 39: Dot Product
.
=
Codelet
A
B

## Slide 40: Dot Product
.
=
movaps xmm0, [basePtr1]
movaps xmm1, [basePtr2]
DPPS xmm0, xmm1, 0xF
Movaps [basePtr3], xmm0
A
B
subA
subB
Sub_res
subDotCod
L0 Codelet definition
Using SSE SIMD ISA

## Slide 41: Dot Product
.
=
A
B
SET , 0
Loop:
BREQ , N , After
LD A[]
LD B[]
subDotCod( , , )
ADD , ,
ADD , 1
BR Loop
After:
subDotCod
Level in hierarchy
Register name at current level
L1 Codelet definition
L0 codelet

## Slide 42: A convolution example

## Slide 43: 1D Convolution
int A[1000], window[10], res[1009];
for (int i = 0; i < 1009; i ++) { // Iterate over res
int val = 0;
for (int j = 9; j >= 0; j --) { // iterate over A
if ( i - 9 + j >= 0 && j - 9 + j <1000)
val + = A[i - 9 + j]*window[j];
}
res[i] = val;
}

## Slide 44: 1D Convolution
A
res
window
1009
0
int A[1000], window[10], res[1009];
for (int i = 0; i < 1009; i ++) { // Iterate over res
int val = 0;
for (int j = 9; j >= 0; j --) { // iterate over A
if ( i - 9 + j >= 0 && j - 9 + j <1000)
val + = A[i - 9 + j]*window[j];
}
res[i] = val;
int A[1000], window[10], res[1009];
for (int i = 0; i < 1009; i ++) { // Iterate over res
int val = 0;
for (int j = 9; j >= 0; j --) { // iterate over A
if ( i - 9 + j >= 0 && j - 9 + j <1000)
val + = A[i - 9 + j]*window[j];
}
res[i] = val;
}

## Slide 45: 1D Convolution
res
window
A
res = A * window
window
A
res

## Slide 46: 1D Convolution
int A[1000], window[10], res[1009];
for (int i = 0; i < 1009; i ++) { // Iterate over res
int val = 0;
for (int j = 9; j >= 0; j --) { // iterate over A
if ( i - 9 + j >= 0 && j - 9 + j <1000)
val + = A[i - 9 + j]*window[j];
}
res[i] = val;
}

## Slide 47: 1D Convolution – tiled
// L2
int A[1000], window[10], res[1009];
int *ptrA_1;
int *ptrA_0;
int *ptrRes_1;
int *ptrRes_0;
int *ptrWin_1;
int *ptrWin_0;
// L1
ptrA_1 = A;
ptrRes_1 = res;
ptrWin_1 = win;
for (int ii = 0; ii < 1009; ii +=100) {
int end = (ii + 100 < 1009 ? 100 : 1009%100);
for (int i = 0; i < end; i ++) {
int val = 0;
// L0
ptrRes_0 = ptrRes_1 + i;
for (int j = 9; j >= 0; j --) {
if ( i - 9 + j >= 0 && j - 9 + j < end) {
ptrWin_0 = ptrWin_1 + j;
ptrA_0 = ptrA_1 + (i - 9 + j);
val + = *ptrA_0 + *ptrWin_0;
}
ptrRes_0 = val;
}
ptrRes_1 += 100;
ptrA_1 += 100;
}

## Slide 48: 1D Convolution Pseudo-code
// L2
int A[1000], window[10], res[1009];
conv_1D(A, window, res, 1009);
// L1
codelet_def conv_1D (int *A, int *Window, int* res, int sizeRes) {
int *ptrA_1;
int *ptrRes_1;
int *ptrWin_1;
ptrA_1 = A;
ptrRes_1 = res;
ptrWin_1 = win;
for (int ii = 0; ii < sizeRes; ii +=100) {
int end = (ii + 100 < sizeRes ? 100 : sizeRes%100);
for (int i = 0; i < end; i ++) {
int val = 0;
single_conv(ptrA_1, ptrWin_1, &val, i, end)
ptrRes_0 = val;
ptrRes_0++;
}
ptrA_1 += 100;
}
}
// L0
codelet_def single_conv( int* ptrA_1, int* ptrWin_1, int* val, int i, int end) {
int *ptrA_0;
int *ptrWin_0;
for (int j = 9; j >= 0; j --) {
if ( i - 9 + j >= 0 && i - 9 + j < end) {
ptrWin_0 = ptrWin_1 + j;
ptrA_0 = ptrA_1 + (i - 9 + j);
val + = *ptrA_0 + *ptrWin_0;
}
}

## Slide 49: 1D Convolution Pseudo-code L2
// L2
int A[1000], window[10], res[1009];
conv_1D(A, window, res, 1009);

## Slide 50: 1D Convolution Pseudo-code L1
// L1
codelet_def conv_1D (int *A, int *Window, int* res, int sizeRes) {
int *ptrA_1;
int *ptrRes_1;
int *ptrWin_1;
ptrA_1 = A;
ptrRes_1 = res;
ptrWin_1 = win;
for (int ii = 0; ii < sizeRes; ii +=100) {
int end = (ii + 100 < sizeRes ? 100 : sizeRes%100);
for (int i = 0; i < end; i ++) {
int val = 0;
single_conv(ptrA_1, ptrWin_1, &val, i, end)
ptrRes_0 = val;
ptrRes_0++;
}
ptrA_1 += 100;
}
}

## Slide 51: 1D Convolution Pseudo-code L0
// L0
codelet_def single_conv( int* ptrA_1, int* ptrWin_1, int* val, int i, int end) {
int *ptrA_0;
int *ptrWin_0;
for (int j = 9; j >= 0; j --) {
if ( i - 9 + j >= 0 && i - 9 + j < end) {
ptrWin_0 = ptrWin_1 + j;
ptrA_0 = ptrA_1 + (i - 9 + j);
val + = *ptrA_0 + *ptrWin_0;
}
}

## Slide 52
L2 Register File
L1 memory
L1
Higher level operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
L1 Register File
L0 memory
L0
Arithmetic operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
To higher level mem
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
L0
To higher levels
L1
L2
// L2
int A[1000], window[10], res[1009];
conv_1D(A, window, res, 1009);
// L1
codelet_def conv_1D (int *A, int *Window, int* res, int sizeRes) {
int *ptrA_1;
int *ptrRes_1;
int *ptrWin_1;
ptrA_1 = A;
ptrRes_1 = res;
ptrWin_1 = win;
for (int ii = 0; ii < sizeRes; ii +=100) {
int end = (ii + 100 < sizeRes ? 100 : sizeRes%100);
for (int i = 0; i < end; i ++) {
int val = 0;
single_conv(ptrA_1, ptrWin_1, &val, i, end)
ptrRes_0 = val;
ptrRes_0++;
}
ptrA_1 += 100;
}
}
// L0
codelet_def single_conv( int* ptrA_1, int* ptrWin_1, int* val, int i, int end) {
int *ptrA_0;
int *ptrWin_0;
for (int j = 9; j >= 0; j --) {
if ( i - 9 + j >= 0 && i - 9 + j < end) {
ptrWin_0 = ptrWin_1 + j;
ptrA_0 = ptrA_1 + (i - 9 + j);
val + = *ptrA_0 + *ptrWin_0;
}
}

## Slide 53
L2 Register File
L1 memory
L1
Higher level operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
L1 Register File
L0 memory
L0
Arithmetic operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
To higher level mem
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
L0
To higher levels
L1
L2

## Slide 54: L2 Codelet ISA description

## Slide 55: L1 Codelet ISA description

## Slide 56: L0 Codelet ISA description

## Slide 57
L2 Register File
L1 memory
L1
Higher level operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
L1 Register File
L0 memory
L0
Arithmetic operations
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
To higher level mem
L0 Register File
ALU + FP
Write Back
SYNC
Memory Access Interface
Scheduling Unit
FETCH
DECODE
L2 Inst Mem
L0
To higher levels
L1
L2